## Slide 1: County of Otsego IDA Broadband Feasibility Study
November 25, 2014

## Slide 2: Opportunity
Deliver broadband access to unserved areas of the County
Dramatic underinvestment over decades by incumbent carriers in the County
  Dial up Internet access in many rural areas
  Limited DSL / cable modem / fixed wireless in parts of rural areas at speeds much less than 10 MB down and 1 MB up
  Satellite providers have costly monthly data packages and bandwidth capacity is limited
Federal and state grant and loan programs available

## Slide 3: Structure
Public Private Partnership
  Potential Partners
    Otsego County
      Tower sites, bonding
    Otsego Electric Cooperative
      Access to poles, construction and maintenance operations
    Telecommunications Provider
      Operational systems and regulatory experience
    County of Otsego IDA
      Grant writing / marketing expertise, PILOT/Property Tax Relief, Financing/Funding partnership and overall Funding Applications/Project coordination

## Slide 4: Structure
Recommend engaging accounting and legal advice to evaluate Cooperative, Non Profit Corporation and other corporate / partnership / joint venture options

## Slide 5: Technology Solution
Hybrid wireless and fiber network
  Initial network provides high speed broadband access to 19,800 (84%) unserved locations
    Hybrid network minimum bandwidth is 10 MB down / 1 MB up
  Ongoing network build out to reach remaining unserved locations (16%)
    Can include larger end user antenna, range extenders, micro cells, new tower sites and additional Fiber To The Premises (FTTx) construction
    May be financed by a combination of additional grants and loans or out of retained earnings

## Slide 6: Technology Solution
Ring 3
Ring 1
Ring 2

## Slide 7: Technology Solution
Hybrid wireless and fiber network
  25 wireless towers connected by fiber backbone
  Wireless fixed broadband access in remote areas of County
    Serves 10,800 locations
    Minimum speed 10 MB down / 1 MB up

## Slide 8: Technology Solution
Hybrid wireless and fiber network
  FTTx solution for community centers, home based businesses, Main Street businesses and residents along the fiber routes
    Fiber backbone includes 3 rings
    210 miles of new fiber
    120 miles of leased existing fiber
    Serves 9,000 locations / 13 community centers
    Minimum 25 MB down / 25 up, Gigabit speeds possible

## Slide 9: Financials
Estimated project cost - $30.3 million
  50% loans including working capital
  50% grants
Profitable operations, positive cash flow throughout the six year projection period
Financial ratio benchmarks met

## Slide 10: Project Summary
Strong customer demand for high speed broadband services
  Drives positive financial projections
Potential partners bring strong experience and assets to the Public Private Partnership
Loan and grants funds are available
Very challenging terrain for both FTTx and fixed wireless services
  Several strategies available to extend service after initial build out plan
Public Private Partnership will develop marketing plan